## Slide 1: FNAL beam test G4 simulation update
Aiwu Zhang
2015-02-02

## Slide 2: Topic 1: Check smearing on trackers
 |  | Ex_exp | In_exp | GM_exp | Ex_G4 | In_G4 | GM_G4 | Corrected resolution
32GeV/c pion case | REF1X | 164 | 44 | 86 | 86 | 23 | 45 | 73
 | REF1Y | 166 | 45 | 87 | 87 | 24 | 45 | 74
 | REF2X | 95 | 66 | 79 | 46 | 32 | 39 | 69
 | REF2Y | 97 | 68 | 81 | 47 | 33 | 39 | 71
 | REF3X | 82 | 50 | 64 | 33 | 20 | 26 | 59
 | REF3Y | 82 | 50 | 64 | 33 | 20 | 26 | 58
 | REF4X | 126 | 55 | 83 | 63 | 27 | 41 | 72
 | REF4Y | 118 | 51 | 78 | 63 | 28 | 42 | 65
As it has been shown, trackers resolution is calculated by subtracting the contribution to residuals due to MCS from the Exp. resolution in quadrature: .
These corrected resolutions are input into post-analysis as a Gaussian smearing on the hit positions.

## Slide 3: Residuals on trackers in X coordinates
REF1
exclusive
REF1
inclusive
REF2
exclusive
REF2
inclusive
Geo. Mean
84um
Geo. Mean
80um

## Slide 4: Residuals on trackers in X coordinates
REF3
exclusive
REF3
inclusive
REF4
exclusive
REF4
inclusive
Geo. Mean
76um
Geo. Mean
79um

## Slide 5: Tracker resolutions
 |  | Geant4 residual width |  |  |  |  |  |  | exp. Data |  |  |  |  | 
 | Smear input | Ex | err | In | err | GM | err |  | Ex | err | In | err | GM | err
REF1X | 73 | 160 | 0.9 | 44 | 0.2 | 84 | 0.7 |  | 164 | 0.7 | 44 | 0.2 | 86 | 0.5
REF1Y | 74 | 163 | 0.9 | 44 | 0.2 | 85 | 0.7 |  | 166 | 0.8 | 45 | 0.2 | 87 | 0.6
REF2X | 69 | 96 | 0.5 | 67 | 0.4 | 80 | 0.6 |  | 95 | 0.4 | 66 | 0.3 | 79 | 0.5
REF2Y | 71 | 99 | 0.5 | 69 | 0.4 | 82 | 0.6 |  | 97 | 0.5 | 68 | 0.4 | 81 | 0.6
REF3X | 59 | 89 | 0.5 | 55 | 0.3 | 70 | 0.5 |  | 82 | 0.4 | 50 | 0.3 | 64 | 0.5
REF3Y | 58 | 86 | 0.5 | 53 | 0.3 | 67 | 0.5 |  | 82 | 0.3 | 50 | 0.2 | 64 | 0.4
REF4X | 72 | 119 | 0.7 | 52 | 0.3 | 79 | 0.6 |  | 126 | 0.6 | 55 | 0.3 | 83 | 0.6
REF4Y | 65 | 115 | 0.7 | 50 | 0.3 | 76 | 0.6 |  | 118 | 0.5 | 51 | 0.2 | 78 | 0.5
In G4, after hit position smearing, we get very similar resolutions compare to the exp. Data.
The table is for 32GeV/c beam. Same conclusion for the 120GeV/c beam.

## Slide 6: Topic 2: Study Geant4 resolution for the FITEIC chamber in polar coordinate (W/O smearing)
FIT_EIC_Phi
Exclusive
FIT_EIC_Phi
Inclusive
 | Offset(mm) |  | Phi resolutions, unit in urad |  |  |  |  |  | R resolutions, unit in um |  |  |  |  | 
 | X | Y | Phi_Ex | err | Phi_In | err | GM_Phi | err | R_Ex | err | R_In | err | GM_R | err
test1 | -500 | 0 | 127 | 0.7 | 101 | 1.0 | 113 | 1.3 | 63 | 0.4 | 50 | 0.3 | 56 | 0.5
test2 | -1000 | 0 | 634 | 0.4 | 51 | 0.3 | 57 | 0.5 | 63 | 0.4 | 50 | 0.3 | 56 | 0.5
 | -1877 | -35 | 34 | 0.2 | 27 | 0.2 | 30 | 0.3 | 63 | 0.4 | 50 | 0.3 | 56 | 0.5
test3 | -5000 | 0 | 13 | 0.1 | 11 | 0.1 | 12 | 0.1 | 63 | 0.4 | 50 | 0.3 | 56 | 0.5
W/o smearing, residual width due to MCS for FITEIC in R is still around 56um. It is not affected by X, Y offsets.
It confirms that relationship of R-resolution and Phi-resolution is roughly:
For the FIT EIC w/ zigzag, HV scanned at X=-1877mm, Y=-35mm, the Phi-resolution is 30urad.

## Slide 7: Geant4 Phi-resolution for the FITEIC (With smearing only trackers)
FIT_EIC_Phi
Exclusive
FIT_EIC_Phi
Inclusive
 | Offset(mm) |  | Phi resolutions, unit in urad |  |  |  |  |  | R resolutions, unit in um |  |  |  |  | 
 | X | Y | Phi_Ex | err | Phi_In | err | GM_Phi | err | R_Ex | err | R_In | err | GM_R | err
test1 | -500 | 0 | 127.2 | 0.7 | 101.0 | 1.0 | 113.3 | 1.3 | 62.6 | 0.4 | 49.7 | 0.3 | 55.8 | 0.5
test2 | -1000 | 0 | 63.9 | 0.4 | 50.6 | 0.3 | 56.9 | 0.5 | 62.5 | 0.4 | 49.7 | 0.3 | 55.7 | 0.5
 | -1877 | -35 | 39 | 0.2 | 31 | 0.2 | 35 | 0.3 | 72 | 0.4 | 58 | 0.3 | 64 | 0.5
Test3 | -5000 | 0 | 13.2 | 0.1 | 10.6 | 0.1 | 11.8 | 0.1 | 62.6 | 0.4 | 49.7 | 0.3 | 55.8 | 0.5
With resolution smearing on the trackers, resolution for the FIT EIC chamber due to MCS effect in phi is ~35urad.
So, by subtracting in quadrature we get

## Slide 8: Geant4 Phi-resolution for the FITEIC (With smearing trackers as well as the FITEIC chamber)
FIT_EIC_Phi
Exclusive
FIT_EIC_Phi
Inclusive
 | Offset(mm) |  | Phi resolutions, unit in urad |  |  |  |  |  | R resolutions, unit in um |  |  |  |  | 
 | X | Y | Phi_Ex | err | Phi_In | err | GM_Phi | err | R_Ex | err | R_In | err | GM_R | err
test1 | -500 | 0 | 127.2 | 0.7 | 101.0 | 1.0 | 113.3 | 1.3 | 62.6 | 0.4 | 49.7 | 0.3 | 55.8 | 0.5
test2 | -1000 | 0 | 63.9 | 0.4 | 50.6 | 0.3 | 56.9 | 0.5 | 62.5 | 0.4 | 49.7 | 0.3 | 55.7 | 0.5
 | -1877 | -35 | 172 | 1.0 | 138 | 0.7 | 154 | 1.2 | 72 | 0.4 | 58 | 0.3 | 64 | 0.5
Test3 | -5000 | 0 | 13.2 | 0.1 | 10.6 | 0.1 | 11.8 | 0.1 | 62.6 | 0.4 | 49.7 | 0.3 | 55.8 | 0.5
Smear FITEIC chamber with 166urad in phi ( and 70um in R).
The resolution comes out to be 154urad, which explains that Geometric mean method gives ~10% over estimation on the resolution when tested detector has worse resolution than trackers.

## Slide 9: Another test on geometric mean method
Smear FITEIC chamber with 166um in X and Y.
The G4 simulation then gives resolutions of ~160um in X and Y, which is 9% better.
This supports that Geometric mean method gives ~10% over estimation on the resolution when tested detector has a much worse resolution than trackers.
Topic 3: looking resolutions in a wider range
Remaining slides:

## Slide 10
Unit:um | ER (EE) | IR | GM | ER | IR | GM | Sqrt(ER^2-EE^2) | smear amount | exp. Data (GM)
Case 1 | not smear REF1 |  |  | smear REF1 |  |  |  |  | 
REF1X | 144 | 39 | 75 | 160 | 44 | 84 | 70 | 73 | 86
REF1Y | 147 | 40 | 77 | 163 | 44 | 85 | 71 | 74 | 87
Case 2 | not smear REF2 |  |  | smear REF2 |  |  |  |  | 
REF2X | 67 | 47 | 56 | 96 | 67 | 80 | 69 | 69 | 79
REF2Y | 68 | 47 | 56 | 99 | 69 | 82 | 71 | 71 | 81
Case 3 | not smear REF3 |  |  | smear REF3 |  |  |  |  | 
REF3X | 67 | 41 | 52 | 89 | 55 | 70 | 58 | 59 | 64
REF3Y | 62 | 38 | 49 | 86 | 53 | 67 | 59 | 58 | 64
Case 4 | not smear REF4 |  |  | smear REF4 |  |  |  |  | 
REF4X | 94 | 41 | 62 | 119 | 52 | 79 | 73 | 72 | 83
REF4Y | 95 | 41 | 62 | 115 | 50 | 76 | 65 | 65 | 78
Case 5 | smearing trackers but not smearing FITEIC |  |  | smearing trackers & FITEIC |  |  |  |  | 
FITEICX | 71 | 57 | 64 | 177 | 142 | 159 | 162 | 166 | 170
FITEICY | 72 | 57 | 64 | 179 | 144 | 161 | 163 | 166 | 170
Tested in XY coordinates for trackers and the FITEIC chamber.
Compared geometric mean method () and error estimation method ().
Errors not shown in the table.

## Slide 11
The trackers are smeared by the amount shown in smear amount column of the previous table.
Smearing the FITEIC chamber from 50 to 290 um with a 10um step, plot the output resolution vs. input resolution (the smeared amount on FITEIC) for both geometric mean method and error estimation method.
Clearly we see (1) error estimation method gives accurate resolutions; (2) geometric mean method underestimates (overestimates) when real resolution is less than 120um (larger than 170um).

## Slide 12
For checking, here all trackers are smeared with a 50 um resolution. The conclusion remains more or less the same.
I think these two plots also explain the reason we observe different resolutions on trackers since the geometric mean method gives worse resolutions at <100um level.

## Slide 13
Study in phi coordinate
Smear trackers with numbers from exp. data
Smear trackers with a 50um resolution